## Slide 1: طراحی کنترل کننده‌ی غیرخطی برای وسایل نقلیه فضایی مجهز به عملگرهای مومنتومی سرعت متغیر علی‌داد قاصر پاییز 96

## Slide 2
ساختارگزارش پروژه
مقدمه
جایروهای کنترل ممان
مدل سازی دینامیکی
قوانین هدایت و شرایط تکینگی
استراتژی های کنترلی
تحلیل و شبیه سازی دینامیک و کنترل
Notes: شماره B1

## Slide 3
مقدمه
کنترل کننده
قانون تکینگی
دینامیک عملگر
دینامیک ماهواره
سنسور
وضعیت
فرمان
وضعیت
فضاپیما
نرخ‌ بدنی سرعت
و بردار وضعیت
اندازه‌گیری و بررسی وضعیت
تصحیح وضعیت
قانون کنترل

## Slide 4
جایروهای کنترل ممان
پارامتر | میکرو-ماهواره | میکرو-ماهواره با CMG
جرم ماهواره (kg) | 50 | 50
عملگر | RW4 | CMG4
اینرسی ماهواره(kg.m2) | (2.5،2.5،2.5) | (2.5،2.5،2.5)
جرم سیستم عملگر(kg) | 4 | 1
توان هر عملگر(W) | 0.8-3.5 | 0.75-4
ولتاژ (v) | 12.-16 | 5.12
حداکثر مومنتوم زاویه‌ای(Nms) | 0.36 | 1.1
حداکثر گشتاور(mNm) | 20 | 52.5
نرخ متوسط چرخش(درجه/ثانیه) | 1.85 | 3
حداقل زمان برای 30 درجه(ثانیه) | 16.17 | 10
عملگر | خروجی | دقت (درجه) | جرم (کیلوگرم) | توان (وات)
گشتاور دهنده‌ی مغناطیسی | 1 تا 4000 Am2 | 1 تا 5 | 0.4 تا 50 | 0.6 تا 16
تراسترهای گاز گرم | 0.5 تا 9000 Nm | 1 تا 5 | متغیر | N/A
تراسترهای گاز سرد | <5 Nm | 1 تا 5 | متغیر | N/A
RW/MW | 0.005 تا 1 Nm | 0.001 تا 1 | 1 تا 20 | 10 تا 110
CMG | 10 تا 500 Nm | 0.001 تا 1 | >1 | 5 تا 150
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 5
1- ژيروسکوپ هاي کنترل ممان تک جيمبال
2- ژيروسکوپ هاي کنترل ممان دو جيمبال
3- ژيروسکوپ هاي کنترل ممان سرعت متغير
جایروهای کنترل ممان
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 6
مدل سازی دینامیکی
پارامترهای تغییر یافته‌ی
رودریگرز
جهت چرخش از مختصات مداری به مختصات بدنی
-حداقل تعداد پارامترها
-سینماتیک کاملا معکوس‌پذیر
کنترل کننده
قانون تکینگی
دینامیک عملگر
دینامیک ماهواره
سنسور
نرخ‌ بدنی سرعت
و بردار وضعیت
وضعیت فرمان
وضعیت فعلی

## Slide 7
مدل سازی دینامیکی
فرضیات
کنترل کننده
قانون تکینگی
دینامیک عملگر
دینامیک ماهواره
سنسور
وضعیت
فرمان
وضعیت
فضاپیما
نرخ‌ بدنی سرعت
و بردار وضعیت
بردار سرعت زاویه ای مداری

## Slide 8
قوانین هدایت و شرایط تکینگی
هدف قانون هدایت بدست آوردن بهترین مسیرهای زاویه‌ی حلقه برای تولید گشتاور مناسب کنترلی مورد نیاز برای انجام مانورهای مطلوب و عبور از میان شرایط تکین می‌باشد.
W=Weight Matric

## Slide 9
استراتژی های کنترلی
روش کنترل بازگشت به عقب
مقاومت در مقابل اختلالات خارجی
روش کنترل مد لغزشی
قابلیت پیاده‌سازی به صورت سیستماتیک و سریع
اطمینان از همگرایی به وضعیت مدنظر با توجه به انتخاب تابع لیاپانف
افزایش دقت کنترل حالت پایدار
وجود چندین ساختار کنترلی متفاوت در رسیدن به مسیر نهایی
دارای طیف گسترده‌ای از حالت‌های عملیاتی مانند تنظیم، کنترل مسیر، مشاهده و تعقیب مدل
تغییرناپذیری ویژگی‌های دینامیکی
دارای مقاومت در مقابل اختلالات خارجی
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 10
استراتژی های کنترلی
روش کنترل بازگشت به عقب
محاسبه متغیر مرحله دوم
رابط دو مرحله
محاسبه متغیر اول
بررسی پایداری به کمک تابع لیاپانف (1)
بررسی پایداری به کمک تابع لیاپانف (2)
محاسبه گشتاور کنترلی Tc
محاسبه بهره‌ها به کمک آنالیز پایداری
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 11
استراتژی های کنترلی
روش کنترل مد لغزشی
تابع اشباع
سطح لغزش
بررسی پایداری به کمک تابع لیاپانف
محاسبه گشتاور کنترلی Tc
محاسبه توابع مورد نیاز جهت مد مانور و پایداری
خطای بردار وضعیت
مدل استاندارد
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 12
تحلیل و شبیه سازی دینامیک و کنترل
پارامتر |  | مقادیر
سرعت زاویه‌ای اولیه ماهواره | Rad/sec | ] 0،0،0 [
نرخ سرعت زاویه‌ای | Rad/sec2 | ]T0،0،0[
زاویه حلقه | Deg | ]0،0،0،0 [
نرخ اولیه زاویه حلقه | Rad/sec2 | ] 0،0،0[
ممان اینرسی ماهواره بدون در نظر داشتن ژیروسکوپ‌ها | Kg.m2 | 
ممان اینرسی | Kg.m2 | 0.13
ممان اینرسی | Kg.m2 | 0.04
ممان اینرسی | Kg.m2 | 0.03
جرم دسته ژیروسکوپ | Kg | 1~
نرخ مجاز قاب | Rad/sec | 2±
مانور پایداری وضعیت |  | [20 10 10]
پارامتر |  | مقادیر
سرعت زاویه‌ای اولیه ماهواره | Rad/sec | ] 0،0،0 [
نرخ سرعت زاویه‌ای | Rad/sec2 | ]T0،0،0[
زاویه حلقه | Deg | ]0،0،0،0 [
نرخ اولیه زاویه حلقه | Rad/sec2 | ] 0،0،0[
ممان اینرسی ماهواره بدون در نظر داشتن ژیروسکوپ‌ها | Kg.m2 | 
ممان اینرسی | Kg.m2 | 0.13
ممان اینرسی | Kg.m2 | 0.04
ممان اینرسی | Kg.m2 | 0.03
جرم دسته ژیروسکوپ | Kg | 1~
نرخ مجاز قاب | Rad/sec | 2±
مانور پایداری وضعیت |  | [20 10 10]
پارامترهای شبیه سازی
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 13
تحلیل و شبیه سازی دینامیک و کنترل
روش بازگشتی
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 14
روش مد لغزشی
تحلیل و شبیه سازی دینامیک و کنترل
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 15
محاسبه سینماتیک براساس پارامترهای تغییریافته رودریگرز
محاسبه دینامیک ماهواره با درنظر گرفتن عدم قطعیت ممان اینرسی
به کارگیری ممان اینرسی عملگر و متغیر فرض کردن آن
بررسی پایداری دو روش کنترلی به کمک تابع لیاپانف
طراحی کنترلر با روش بازگشتی در دو مرحله
طراحی کنترلر با مد لغزشی
بررسی و اعتبارسنجی دو روش با روش بازخوردی
یکسان سازی سرعت چرخ ها طبق منطق هدایت
آنچه در این کد خواهید آموخت
Notes: For example, the attitude control
subsystem engineer can take the orbital characteristics and compute the on-orbit disturbance
torques produced for a given spacecraft configuration, which in turn determines
the angular momentum profile

## Slide 16: نکات و الزامات
1- این برنامه در همه نسخه های متلب قابل اجراست.
2- خروجی ها در همه نسخه های متلب سیمولینک قابل مشاهده است.
3- آشنایی تخصصی با دینامیک و کنترل فضاپیما .
4- آشنایی با کنترلرهای غیرخطی بازگشت به عقب.

## Slide 17: مراجع
A. D. Jacot and D. J. Liska. "Control moment gyros in attitude control." Journal of Spacecraft and Rockets, Vol. 3, No. 9 (1966), pp. 1313-1321.
Bedrossian, N. S., Paradiso, J. A., and Bergman, E., “Steering Law Design for Redundant Single-Gimbal Control Moment Gyroscopes,” Journal of Guidance,Control and Dynamics, Vol. 13, No. 6, 1991, pp. 1113-1119
Wie, B. 1998,Space Vehicle Dynamics and Control, AIAA Education series
Nakamura, Y. and Hanafusa, H., “Inverse Kinematic Solutions with Singularity Robustness for Robot Manipulator Control,” Journal of Dynamic Systems, Measurement, and Control, Vol. 111, Sept. 1916, pp. 164–171.
Richie, D. J., P. Tsiotras, and J. L.Fausz, June 25-27, 2001, “Simultaneous attitude Control and Energy Storage Using VSCMGs: Theory and Simulation,” Proceedings of the American Control Conference, Arlington, VA, pp. 3973-3979.
V.J. Lappas, WH Steyn, C.I. Underwood, Practical Results on the Development of a Control Moment Gyro based Attitude Control System for Agile Small Satellites , 2002
V. Lappas, Dr. WH Steynb, Dr. CI Underwood, Attitude Control for Small Satellites using Control Moment Gyros, 2002
V. Lappas , A Control Moment Gyro (CMG) Based Attitude Control System (ACS) For Agile Small Satellites, ,2002
Lappas V, Wie B. 'Robust CMG steering logic with gimbal angle constraints'. Collection of Technical Papers - AIAA/AAS Astrodynamics Specialist Conference, 2006, 2, pp. 1425-1438.
D. J. Richie, V. J. Lappas, and G. Prassinos, “Sizing/Optimization of a Small Satellite Energy Storage and Attitude Control System,” Journal of Spacecraft and Rockets, Vol. 44, July–August 2007, pp. 940–952.
D. J. Richie, V. J. Lappas, and G. Prassinos, “A Practical Small Satellite Variable-Speed Control Moment Gyroscope For Combined Energy Storage and Attitude Control,” AAS/AIAA Astrodynamics Specialist Conference, Honolulu, Hawaii, Aug. 18-21 2008. Paper No. AIAA-2008–7503.
M. Takahashi , Y. Nanamori and K. Yoshida , “Rapid Multi-target Pointing and High Accuracy Attitude Control Steering Law of Variable Speed Control Moment Gyroscopes”, AIAA 2008-7015
Hyungjoo Yoon and Brij N. Agrawal,Adaptive Control of Uncertain Hamiltonian Multi-Input Multi-Output Systems: With Application to Spacecraft Control, 063-6536/$25.00 © 2009 IEEE
K. Sangwon, PhD Thesis, "Attitude Control of Small Satellites Using Single-Gimbal Control Moment Gyros", Feb. 2010
D.KIM,PhD Thesis, “A Novel Integrated Spacecraft Attitude Control System Using Variable Speed Control Moment Gyroscopes: A Lyapunov-Based Approach”, University of Florida,2011
Shuster M.D., “A survey of attitude representations”, The Journal of Astronautical Sciences, Vol 41, No 4, 1993, pp 439 – 517
Khalil H.K., “Nonlinear Systems, Second Edition”, Prentice Hall, 1996
Mohammed Arezki Si Mohammed, Simulation of Three Axis Attitude Control Using a Control Momentum for Small Satellites, July 4 - 6, 2012, London, U.K.
Kristiansen R., Nicklasson PJ., “Satellite attitude control by quaternion basedbackstepping”, American Control Conference, 2005, W-B11-4, pp 907 – 912.
Hyungjoo Yoon, phD Thesis, Spacecraft Attitude and Power Control Using Variable Speed Control Moment Gyros, December 2006.
Hyungjoo Yoon and Panagiotis Tsiotras, Spacecraft Adaptive Attitude and Power Tracking with Variable Speed Control Moment Gyroscopes, journal of guidance, control, and dynamics Vol. 25, No. 6, November–December 2002.
Daan Stevenson and Hanspeter Schaub, Nonlinear control analysis of a double gimbal variable-speed control moment gyro, AAS 11-567,2011.
Takaya Inamori, Nobutada Sako ,Shinichi Nakasuka,Compensation of time-variable magnetic moments for a precise attitude control in nano- and microsatellite missions, Advances in Space Research 48 (2011) 432–440.

## Slide 18: مراجع
Hyungjoo Yoon and Brij N. Agrawal,Adaptive Control of Uncertain Hamiltonian Multi-Input Multi-Output Systems: With Application to Spacecraft Control, 063-6536/$25.00 © 2009 IEEE.
Jessica Gersh and Mason Peck, Violet: A High-Agility Nanosatellite for Demonstrating small Control-Moment Gyroscope Prototypes and Steering Laws, Cornell University, Ithaca, NY, 14850,AIAA 2009-5900.
Frederick Aaron Leve,Development of the spacecraft orientation buoyancy experimental kiosk, Thesis, University of Florida, 2008.
David J. Richie, Panagiotis Tsiotras ,Jerry L. Fausz, Variable speed control moment gyroscope workbench: A new simuation tool for tomorrow’s spacecraft, 2001.
Berner, R., Control Moment Gyro Actuator for Small Satellite Application, M. s. Thesis, University of Stellenbosch, 2005.
Vaios J. Lappas , A Control Moment Gyro (CMG) Based Attitude Control System (ACS) For Agile Small Satellites, ,2002.
R. O. doruk, “nonlinear controller designs for a reaction wheel actuated observatory satellite”, PhD Thesis, June 2008.
P. Tsiotras, H. Shen, and C. Hall, “Satellite Attitude Control and Power Tracking with Energy/Momentum Wheels,” Journal of Guidance, Control, and Dynamics, Vol. 24, No. 1, 2001, pp. 23–24.
Masaki Takahashi, Yasuyuki Nanamori and Kazuo Yoshida, Rapid Multi-target Pointing and High Accuracy Attitude Control Steering Law of Variable Speed Control Moment Gyroscopes, AIAA 2008-7015.
Wiley J. Larson, James R. Wertz, editeur, Space Mission Analysis and Design, Vol. 7th printing, Space Technology Library/Microcosm Press, third édition, 2005.
Alger, Michael William Richard. Design and Development of Power and Attitude Control Subsystems for Ryesat. Master’s thesis, Ryerson University, 2006.
B. Wie, H. Weiss, & Arapostathis, A., “Quaternion Feedback Regulator for Spacecraft Eigenaxis Rotations,” Journal of Guidance, Control, and Dynamics, Vol. 12, No. 3, May-June, 1989, Pages: 375–380.
Sidi, M. J., Spacecraft Dynamics and Control, Cambridge University Press, Cambridge, UK, 1997.
Tsiotras, P., Yoon, H., and Marshall, A., “Controllability Analysis and Control of Spacecraft Using a Single-Gimbal Variable-Speed Control Moment Gyroscope,” Internal Report, School of Aerospace Engineering, Georgia Institute of Technology, Atlanta, GA, January 2004.
Marshall, A., and Tsiotras, P., “Spacecraft Angular Velocity Stabilization Using a Single-Gimbal Variable Speed Control Moment Gyro,” AIAA Paper 03-5654, 2003.
Ford, K. A. and Chris Hall, 2000, “Singular Direction Avoidance Steering for Control-Moment Gyros,” AIAA Journal of Guidance, Control, and Dynamics, Vol 23, No. 4, pp. 648-656.
Kurokawa, H., “Constrained steering law of pyramid-type control moment gyros and ground tests,” Journal of Guidance, Control, and Dynamics, vol. 20, no. 3, pp.445– 449, 1997.

## Slide 19
با تشکر از توجه شما